## Slide 1: Tutorial Permeability

## Slide 2: Backend
Python 3.6 or higher
Packages:
  Pydicom
  Numpy
  Matplotlib
  Pandas

## Slide 3: Usage
Open the terminal
Make sure the program and the related files are in the same folder

## Slide 4: Usage
Type python permeability –wd [file dir]

## Slide 5: Usage
rename
  Do every time when execute the program
  This will generate a new folder to store renamed file and change the working folder to the new folder
select [slice num] [label] [--manual-radius] [--manual-input] center.x, center.y, radius
  Slice num and label is necessary
  --manual-radius : default 5 or determined by user
  --manual-input : input given center and radius manully
  Example:
    select 601 RF –-manual-radius 7
    select 601 RF (this will open a new window to select ROI)
    select 601 RF –manual-input 50 70 3 (centered at 50, 70 radius 3)

## Slide 6: Usage
clean [region label]
  If the selection is incorrect, type clean [region label]
  For example: clean RF
inputfile [filename]
  If you have a reference file, please use this function
print [region] [result] [fat]
  You can show some information by using this function
computation –all [series number]
  Main function for computation
  Series number is necessary, provide the program to know how many images are in a study

## Slide 7: Usage
stat –all
  This function is to show some computation results after the Ki’s are computed in each ROI
  It will also store the final result.

## Slide 8: Simple usage
If you don’t have a reference file:
rename
pid [pid]
select [number] [label]
satisfied?
computation –all [series number]
stat –all
clean [label]
Y
N

## Slide 9: Simple usage
If you have a reference file:
rename
pid [pid]
inputfile [filename]
computation –all [series number]
stat –all